## Slide 1
LECTURE WEEK 8
PART I
FIT3143
INTRODUCTION TO INSTRUCTION LEVEL PARALLELISM (ILP) PROCESSORS

## Slide 2: Overview
Evolution and overview of ILP Processors
Understanding of inter-instruction dependencies
  Data, Control and Resource Dependencies
What is instruction Scheduling?
Sequential Consistency
How fast can we go?
Learning outcome(s) related to this topic
Explain the fundamental principles of parallel computing architectures and algorithms (LO1)

## Slide 3: Evolution of ILP Processors
Increasing processor performance has been provided by increased Instruction Level Parallelism (ILP)

## Slide 4: Instruction Level Parallelism
Consider following code fragment
  mul r3, r4  r8
  add r1, r2  r7
  load r6,(r1)
  add #5, r5
Which instructions are unrelated?
  Can be executed in any order
load r6,(r1)
mul r3,r4  r8
add r1,r2  r7
add #5,r5

## Slide 5: Pipelining or parallel?
Pipelined operation
Pipelined processors
Parallel operation
Very Long Instruction Word (VLIW) and
Super scalar processors
Internal operating principle of IFP processors
FU
1
FU
2
FU
m
FU
1
FU
2
FU
m
FU: functional unit
Notes: Instruction Fetch Pipeline
Functional Unit
Very Long Instruction Word

## Slide 6: Pipelining
Fetch
Decode
Execute
Writeback
Cache/ Memory
Funit
Dunit
Eunit
tc
tc
tc
tc
Fstage
Dcycle
Estage
Wstage
Register
File
time

## Slide 7: Machine Utilisation with pipelining
Instr. 1
Instr. 2
Instr. 3
Instr. 4
Instr. 5
Instr. 6
Instr. 7
Machine
BUSY
F1
F2
D1
F3
D2
E1
F4
D3
E2
W1
F5
D4
E3
W2
F6
D5
E4
W3
F7
D6
E5
W4
time
Notes: The aim is to cancel out CPU idle time by always having sufficient workload in the pipeline.

## Slide 8: VLIW Approach
Software scheduling
Parallel execution
Multiple ports to registers
Multiple instructions /word
Register
File
Fetch
Unit
Cache/
Memory
EU
EU
EU
EU
Notes: Multiple dispatch ports, cache ports, register ports

## Slide 9: Superscalar Approach
Hardware scheduling
Parallel execution
Multiple ports to registers
Dynamic Scheduling
Register
File
Fetch
Unit
Cache/
Memory
EU
EU
EU
EU

## Slide 10: Out-of-order Execution (OOOE)
Look ahead in a window of instructions and find instructions that are ready to execute
  Don’t depend on data from previous instructions still not executed
  Resources are available
Out-of-order execution
  Start instruction execution before execution of a previous instructions
Advantages:
  Help exploit Instruction Level Parallelism (ILP)
  Help cover latencies (e.g., L1 data cache miss, divide)
Can Compilers do the work ?
  Compilers can statically reschedule instructions
  Compilers do not have run time information
    Conditional branch direction → limited to basic blocks
    Data values, which may affect calculation time and control
    Cache miss / hit

## Slide 11: Dependencies between instructions
Data Dependencies
  Future instructions depend on results of prior ones
  Registers and Memory
Control Dependencies
  Branch dependencies
Resource Dependencies
  Number of ALUs, memory ports, etc
Notes: ALU arithmetic logic unit

## Slide 12: Data Dependencies
Data Dependencies in straight line code
Read After Write
dependency
(flow dependency)
Write After Read
dependency
(Anti-dependency)
Write After Write
dependency
(Output dependency)
Load-use
dependency
Define-use
dependency
True dependency
(Cannot be abandoned)
False dependency
(Can be eliminated by register renaming)

## Slide 13: Data Flow Analysis
Example
; r1 depends on (1)
; r5 is independent
; r6 & r3 are independent
; r5 depends on (3); r6 depends on (4)
; r8 depends on (2); r4 depends on (5)

## Slide 14: OOOE – General Scheme
Fetch & decode instructions in parallel but in order, to fill instruction pool
Execute ready instructions from the instructions pool
  All the data required for the instruction is ready
  Execution resources are available
Once an instruction is executed
  signal all dependant instructions that data is ready
Commit instructions in parallel but in-order
  Can commit an instruction only after all preceding instructions (in program order) have committed

## Slide 15: Example
Assume that executing a divide operation takes 20 cycles
Inst2 has a RAW dependency on r1 with Inst1
  It cannot be executed in parallel with Inst1
Can successive instructions pass Inst2 ?
  Inst3 cannot since Inst2 must read r8 before Inst3 writes to it
  Inst4 cannot since it must write to r3 after Inst2
  Inst5 can

## Slide 16: False Dependencies
OOOE creates new dependencies
  WAR: write to a register which is read by an earlier inst.
  WAW: write to a register which is written by an earlier inst.
These are false dependencies
  There is no missing data
  Still prevent executing instructions out-of-order
Solution: Register Renaming

## Slide 17: Register Renaming
Hold a pool of physical registers
Map architectural registers into physical registers
  Before an instruction can be sent for execution
    Allocate a free physical register from a pool
    The physical register points to the architectural register
  When an instruction writes a result
    Write the result value to the physical register
  When an instruction needs data from a register
    Read data from the physical register allocated to the latest inst which writes to the same arch register, and precedes the current instruction
    If no such instruction exists, read directly from the arch register
  When an instruction commits
    Move the value from the physical register to the arch register it points

## Slide 18: Example
Register Renaming Benefits
Removes false dependencies
Removes architecture limit for # of registers

## Slide 19: Mapping to Physical Registers
r1, r2, … , r6 is referring to the architectural register while r1', r1'' etc. are referring to physical registers. There can be multiple of them, depending on the processor.
The results from each instruction will only be committed to the architectural registers in the in-order retirement stage.
(1) r1  mem1 r1’  mem1
(2) r2  r2 + r1 r2’  r2 + r1’
(3) r1  mem2 r1’’  mem2
(4) r3  r3 + r1 r3’  r3 + r1’’
(5) r1  mem3 r1’’’  mem3
(6) r4  r5 + r1 r4’  r5 + r1’’’
(7) r5  2 r5’  2
(8) r6  r5 + 2 r6’  r5’ + 2
Cycle 1
Cycle 2
Map to physical register
Register renaming (map to another physical register)

## Slide 20: Executing Beyond Branches
So far we do not look for instructions ready to execute beyond a branch
Limited to the parallelism within a basic-block
  A basic-block is ~5 instruction long
We would like to look beyond branches
  But what if we execute an instruction beyond a branch and then it turns out that we predicted the wrong path ?
Solution: Speculative Execution

## Slide 21: Speculative Execution
Execution of instructions from a predicted (yet unsure) path
  Eventually, path may turn wrong
Implementation:
  Hold a pool of all not yet executed instructions
    Fetch instructions into the pool from a predicted path
  Instructions for which all operands are ready can be executed
  An instruction may change the processor state (commit) only when it is safe
    An instruction commits only when all previous (in-order) instructions have committed instructions commit in-order
    Instructions which follow a branch commit only after the branch commits
      If a predicted branch is wrong all the instructions which follow it are flushed
Register Renaming helps speculative execution
  Renamed registers are kept until speculation is verified to be correct

## Slide 22: Example
Instructions 6-9 are speculatively executed
  If the prediction turns wrong, they will be flushed
If the branch was predicted taken
  The instructions from the other path would be have been speculatively executed

## Slide 23: Data Dependencies in Loops
Not all data dependencies are obvious by examining the source code.
Consider
  do I = 2, n
    X(I) = A*X(I-1) + B
Recurrence between iteration I and I-1
Compiler needs to analyze loop expressions to detect and handle recurrences correctly.
Notes: Note, the previous iteration value of X(I) is being used to calculate the current iteration’s X(I) value. Compiler if pipelining must consider the loop recurrence. The write in I-1 iteration must complete before read of Ith iteration begins – breaks standard pipelining scheme

## Slide 24: Control Dependencies
Consider the following code
  mul r1, r2  r3
  jz zproc
  sub r4, r1  r1
  :
  zproc: load r1, x
  :
Branch depends on
Result of “mul”
What happens if we
prefetch this
instruction?
What happens if we
DON’T
Prefetch this instruction?
Notes: Prefetching occurs when a processor requests an instruction from main memory before it is actually needed.
Ans1: invalid r1 value will be used.
Ans2: There will be wait introduced.

## Slide 25: Is this a problem?
Ratio of branches
  General Purpose 22 % to 39%
  Scientific 5% - 11 %
Conditional to unconditional
  General Purpose 46% to 83%
  Scientific 53 % to 83 %
For 25% 1 in 4 instruction is a branch
Effect on pipeline?

## Slide 26: Impact on ILP processors
JC
JC
JC
JC
JC
JC
JC
JC
JC
JC
JC
JC
scalar issue
superscalar (or VLIW)
issue
2 intructions/issue
3 intructions/issue
6 intructions/issue
t
JC: conditional branch

## Slide 27: Resource Dependencies
Consider the following code
  div r1, r2  r3
  div r4, r2  r5
Insufficient dividers to issue both instructions in parallel
Possible resources
  buses, execution units, buffers (storage slots)

## Slide 28: Instruction scheduling
When instructions are processed (that is, issued, renamed, executed and so forth) in parallel, it is often necessary to detect and resolve dependencies between instructions.
Three main approaches
  Static scheduling
  Dynamic scheduling
  Hybrid

## Slide 29: Static vs Dynamic scheduling
ILP
Compiler
Software
Window
Dependency
Free code
for ILP
Super scalar
VLIW
Input code
Notes: ILP compiler determines the parallelism for VLIW

## Slide 30: Static vs Dynamic scheduling ...
Instruction
Issue unit
Issue
Window
Dependency
Free
instruction issue
Pipelined
Superscalar
Input code
Execution
Window
Notes: Superscaler determines parallelism from dependency free instruction issue (dynamically). Pipelined simply executes in sequence (with pipelining).

## Slide 31: ILP Instruction Scheduling
Static Scheduling boosted by parallel code optimisation
  Performed entirely by the compiler
  Processor receives dependency-free and optimized code for parallel execution
  Typical for VLIW and a few pipelined processors (e.g. MIPS)
Notes: Microprocessor without Interlocked Pipeline Stages) is a reduced instruction set computing (RISC) instruction set architecture (ISA) developed by MIPS Computer Systems (now MIPS Technologies).

## Slide 32: ILP Instruction Scheduling
Dynamic Scheduling without static parallel code optimisation
  Performed entirely by the processor
  The code is not optimised for parallel execution. The Processor detects and resolves dependencies on its own
  Early ILP processors (e.g. CDC 6600, IBM 360/91)

## Slide 33: ILP Instruction Scheduling
Dynamic scheduling boosted by static parallel code optimisation
  Performed by the processor in conjunction with the parallel optimizing compiler
  The processor receives optimised code for parallel execution, but it detects and resolves dependencies of its own
  Usual practice for pipelined superscalar processors (e.g. RS/6000, PL.8/XL, i960 and QTC SF960)

## Slide 34: Preserving Sequential Consistency
When instructions are executed in parallel, processor must be careful to preserve the sequential consistency.
  div r1, r2  r3
  add r5, r6  r7
  jz anywhere
Must make sure the jz instruction uses the condition codes set by the add, not the div which might take longer.

## Slide 35: Types of consistency
Strong consistency
  Preserves the actual execution order
Weak consistency
  Produces correct result
  Can execute out of order providing the code still delivers the correct result

## Slide 36: How fast can we go?
Performance is limited by
  underlying algorithm (dependencies)
  compiled code (false dependencies, staging)
  actual hardware (resource restrictions)
Study all three to work out maximum speedup

## Slide 37: How fast can we go? Earliest methods to achieve speed ups for scientific programs

## Slide 38: How fast can we go? Earliest methods to achieve speed ups for scientific programs

## Slide 39: Effect of register renaming

## Slide 40: Summary
Evolution and overview of ILP Processors
  Pipelines, VLIW or super scaler
Understanding of inter-instruction dependencies
  Data, Control and Resource Dependencies
Instruction Scheduling
  Static & Dynamic scheduling
Sequential Consistency
  When instructions are executed in parallel, processor must be careful to preserve the sequential consistency.
How fast can we go?
  Performance is limited by underlying algorithm compiled code and actual hardware (resource restrictions)

## Slide 41: References
  Sima .D, Fountain .T, Karsuk .P, “Chapter 4: Introduction to ILP-Processors”, in Advanced Computer Architectures – A Design Space Approach, Addison Wesley Longman, 1997, pp. 113 – 135.